## Slide 1: Chapter #8: Finite State Machine Design Contemporary Logic Design Randy H. Katz University of California, Berkeley June 1993

## Slide 2: Chapter 8: Finite State Machine Design
Motivation

## Slide 3: Motivation
• Counters: Sequential Circuits where State = Output
• Generalizes to Finite State Machines:
Outputs are Function of State (and Inputs)
Next States are Functions of State and Inputs
Used to implement circuits that control other circuits
"Decision Making" logic
• Application of Sequential Logic Design Techniques
Word Problems
Mapping into formal representations of FSM behavior
Case Studies

## Slide 4: Chapter Overview
Concept of the State Machine
• Partitioning into Datapath and Control
• When Inputs are Sampled and Outputs Asserted
Basic Design Approach
• Six Step Design Process
Alternative State Machine Representations
• State Diagram, ASM Notation, VHDL, ABEL Description Language
Moore and Mealy Machines
• Definitions, Implementation Examples
Word Problems
• Case Studies

## Slide 5: Concept of the State Machine
Computer Hardware = Datapath + Control
Registers
Combinational Functional
Units (e.g., ALU)
Busses
FSM generating sequences
of control signals
Instructs datapath what to
do next
"Puppet"
"Puppeteer who pulls the
strings"
Qualifiers
Control
Control
Datapath
State
Control
Signal
Outputs
Qualifiers
and
Inputs

## Slide 6: Concept of the State Machine
Example: Odd Parity Checker
Assert output whenever input bit stream has odd # of 1's
State
Diagram
Symbolic State Transition Table
Encoded State Transition Table

## Slide 7: Concept of the State Machine
Example: Odd Parity Checker
Next State/Output Functions
NS = PS xor PI; OUT = PS
D FF Implementation
T FF Implementation
Timing Behavior: Input 1 0 0 1 1 0 1 0 1 1 1 0

## Slide 8: Concept of State Machine
Timing:
When are inputs sampled, next state computed, outputs asserted?
State Time: Time between clocking events
• Clocking event causes state/outputs to transition, based on inputs
• For set-up/hold time considerations:
Inputs should be stable before clocking event
• After propagation delay, Next State entered, Outputs are stable
NOTE: Asynchronous signals take effect immediately
Synchronous signals take effect at the next clocking event
E.g., tri-state enable: effective immediately
sync. counter clear: effective at next clock event

## Slide 9: Concept of State Machine
Example: Positive Edge Triggered Synchronous System
On rising edge, inputs sampled
outputs, next state computed
After propagation delay, outputs and
next state are stable
Immediate Outputs:
affect datapath immediately
could cause inputs from datapath to change
Delayed Outputs:
take effect on next clock edge
propagation delays must exceed hold times

## Slide 10: Concept of the State Machine
Communicating State Machines
Machines advance in lock step
Initial inputs/outputs: X = 0, Y = 0
One machine's output is another machine's input

## Slide 11: Chapter 8: Finite State Machine Design
Basic Design Approach

## Slide 12: Basic Design Approach
Six Step Process
1. Understand the statement of the Specification
2. Obtain an abstract specification of the FSM
3. Perform a state mininimization
4. Perform state assignment
5. Choose FF types to implement FSM state register
6. Implement the FSM
1, 2 covered now; 3, 4, 5 covered later;
4, 5 generalized from the counter design procedure

## Slide 13: Basic Design Approach
Example: Vending Machine FSM
General Machine Concept:
deliver package of gum after 15 cents deposited
single coin slot for dimes, nickels
no change
Block Diagram
Step 1. Understand the problem:
Draw a picture!

## Slide 14: Vending Machine Example
Tabulate typical input sequences:
three nickels
nickel, dime
dime, nickel
two dimes
two nickels, dime
Draw state diagram:
Inputs: N, D, reset
Output: open
Step 2. Map into more suitable abstract representation

## Slide 15: Vending Machine Example
Step 3: State Minimization
reuse states
whenever
possible
Symbolic State Table

## Slide 16: Vending Machine Example
Step 4: State Encoding

## Slide 17: Parity Checker Example
Step 5. Choose FFs for implementation
D FF easiest to use
D1 = Q1 + D + Q0 N
D0 = N Q0 + Q0 N + Q1 N + Q1 D
OPEN = Q1 Q0
8 Gates
K-map for Open
K-map for D0
K-map for D1
Q0
Q1 Q0
D N
Q1
Q0
D
N
Q1 Q0
D N
Q1
Q0
D
N
Q1 Q0
D N
Q1
D
N
1
0
1
1
0
1
1
1
X
X
X
X
00
01
11
10
1
1
1
1
00
01
11
10
00
01
11
10
00
01
11
10
0
0
0
1
1
1
1
0
X
X
X
X
1
1
1
0
00
01
11
10
00
01
11
10
0
0
0
1
0
0
0
1
X
X
X
X
0
0
0
1

## Slide 18: Parity Checker Example
Step 5. Choosing FF for Implementation
J-K FF
Remapped encoded state transition table

## Slide 19: Vending Machine Example
Implementation:
J1 = D + Q0 N
K1 = 0
J0 = Q0 N + Q1 D
K0 = Q1 N
7 Gates
K-map for K1
K-map for J1
Q1 Q0
D N
Q1
Q0
D
N
Q1 Q0
D N
Q1
Q0
D
N
K-map for K0
K-map for J0
Q1 Q0
D N
Q1
Q0
D
N
Q1 Q0
D N
Q1
Q0
D
N
00
10
11
01
00
10
11
01
00
10
11
01
00
10
11
01
00
10
11
01
00
10
11
01
00
10
11
01
00
10
11
01
0
0
X
X
X
X
0
1
X
X
X
X
X
X
1
1
X
X
0
0
X
X
0
0
X
X
X
X
X
X
0
0
0
X
X
0
X
X
1
1
X
X
X
X
X
X
X
X
0
X
X
1
X
X
0
0
X
1
0
X
X
0
0
X

## Slide 20: Alternative State Machine Representations
Why State Diagrams Are Not Enough
Not flexible enough for describing very complex finite state machines
Not suitable for gradual refinement of finite state machine
Do not obviously describe an algorithm: that is, well specified
sequence of actions based on input data
algorithm = sequencing + data manipulation
separation of control and data
Gradual shift towards program-like representations:
• Algorithmic State Machine (ASM) Notation
• Hardware Description Languages (e.g., VHDL)

## Slide 21: Alternative State Machine Representations
Algorithmic State Machine (ASM) Notation
Three Primitive Elements:
• State Box
• Decision Box
• Output Box
State Machine in one state
block per state time
Single Entry Point
Unambiguous Exit Path
for each combination
of inputs
Outputs asserted high (.H)
or low (.L); Immediate (I)
or delayed til next clock

## Slide 22: Alternative State Machine Representations
ASM Notation
Condition Boxes:
Ordering has no effect on final outcome
Equivalent ASM charts:
A exits to B on (I0 • I1) else exit to C

## Slide 23: Alternative State Machine Representations
Example: Parity Checker
Nothing in output list implies Z not asserted
Z asserted in State Odd
Input X, Output Z
Input
F
T
F
T
Present
State
Even
Even
Odd
Odd
Next
State
Even
Odd
Odd
Even
Output
—
—
A
A
Symbolic State Table:
Input
0
1
0
1
Present
State
0
0
1
1
Next
State
0
1
1
0
Output
0
0
1
1
Encoded State Table:
Trace paths to derive
state transition tables

## Slide 24: Alternative State Machine Representations
ASM Chart for Vending Machine

## Slide 25: Chapter 8: Finite State Machine Design
Mealy and Moore

## Slide 26: Moore and Mealy Machine Design Procedure
Definitions
Moore Machine
Outputs are function
solely of the current
state
Outputs change
synchronously with
state changes
Mealy Machine
Outputs depend on
state AND inputs
Input change causes
an immediate output
change
Asynchronous signals

## Slide 27: Moore and Mealy Machines
State Diagram Equivalents
Outputs are associated
with State
Outputs are associated
with Transitions
Moore
Machine
Mealy
Machine

## Slide 28: Moore and Mealy Machines
States vs. Transitions
Mealy Machine typically has fewer states than Moore Machine
for same output sequence
Equivalent
ASM Charts
Same I/O behavior
Different # of states
S0
S1
IN
IN
S2
IN
10
01
00
H.OUT
S0
S1
IN
IN
1
0
H.OUT
F
F
T
T
F
T
F
T
F
T

## Slide 29: Moore and Mealy Machines
Timing Behavior of Moore Machines
Reverse engineer the following:
Input X
Output Z
State A, B = Z
Two Techniques for Reverse Engineering:
• Ad Hoc: Try input combinations to derive transition table
• Formal: Derive transition by analyzing the circuit

## Slide 30: Moore and Mealy Machines
Ad Hoc Reverse Engineering
Behavior in response to input sequence 1 0 1 0 1 0:
Partially Derived
State Transition
Table

## Slide 31: Moore and Mealy Machines
Formal Reverse Engineering
Derive transition table from next state and output combinational
functions presented to the flipflops!
Ja = X
Jb = X
Ka = X • B
Kb = X xor A
Z = B
FF excitation equations for J-K flipflop:
A+ = Ja • A + Ka • A = X • A + (X + B) • A
B+ = Jb • B + Kb • B = X • B + (X • A + X • A) • B
Next State K-Maps:
State 00, Input 0 -> State 00
State 01, Input 1 -> State 01
A+
B+
AB
X
00
01
11
10
0
1
AB
X
00
01
11
10
0
1
0
0
1
1
0
1
1
0
0
0
0
1
1
1
0
1

## Slide 32: Moore and Mealy Machines
Complete ASM Chart for the Mystery Moore Machine
Note: All Outputs Associated With State Boxes
No Separate Output Boxes — Intrinsic in Moore Machines

## Slide 33: Moore and Mealy Machines
Reverse Engineering a Mealy Machine
Input X, Output Z, State A, B
State register consists of D FF and J-K FF

## Slide 34: Moore and Mealy Machine
Ad Hoc Method
Signal Trace of Input Sequence 101011:
Note glitches
in Z!
Outputs valid at
following falling
clock edge
Partially completed
state transition table
based on the signal
trace

## Slide 35: Moore and Mealy Machines
Formal Method
A+ = B • (A + X) = A • B + B • X
B+ = Jb • B + Kb • B = (A xor X) • B + X • B
= A • B • X + A • B • X + B • X
Z = A • X + B • X
Missing Transitions and Outputs:
State 01, Input 0 -> State 01, Output 1
State 10, Input 0 -> State 00, Output 0
State 11, Input 1 -> State 11, Output 1
A+
B+
Z

## Slide 36: Moore and Mealy Machines
ASM Chart for Mystery Mealy Machine
S0 = 00, S1 = 01, S2 = 10, S3 = 11
NOTE: Some Outputs in Output Boxes as well as State Boxes
This is intrinsic in Mealy Machine implementation

## Slide 37: Moore and Mealy Machines
Synchronous Mealy Machine
latched state AND outputs
avoids glitchy outputs!

## Slide 38: Chapter 8: Finite State Machine Design
Word Problems

## Slide 39: Finite State Machine Word Problems
Mapping English Language Description to Formal Specifications
Four Case Studies:
• Finite String Pattern Recognizer
• Complex Counter with Decision Making
• Traffic Light Controller
• Digital Combination Lock
We will use state diagrams and ASM Charts

## Slide 40: Finite State Machine Word Problems
Finite String Pattern Recognizer
A finite string recognizer has one input (X) and one output (Z).
The output is asserted whenever the input sequence …010…
has been observed, as long as the sequence 100 has never been
seen.
Step 1. Understanding the problem statement
Sample input/output behavior:
X: 00101010010…
Z: 00010101000…
X: 11011010010…
Z: 00000001000…

## Slide 41: Finite State Machine Word Problems
Finite String Recognizer
Step 2. Draw State Diagrams/ASM Charts for the strings that must be
recognized. I.e., 010 and 100.
Moore State Diagram
Reset signal places
FSM in S0
Outputs 1
Loops in State
S0
[0]
S1
[0]
S2
[0]
S3
[1]
S4
[0]
S5
[0]
S6
[0]
Reset
0
1
0
1
0
0
0,1

## Slide 42: Finite State Machine Word Problems
Finite String Recognizer
Exit conditions from state S3: have recognized …010
if next input is 0 then have …0100!
if next input is 1 then have …0101 = …01 (state S2)
S0
[0]
S1
[0]
S2
[0]
S3
[1]
S4
[0]
S5
[0]
S6
[0]
Reset
0
1
0
1
0
0
0,1
1
0
…010
…100

## Slide 43: Finite State Machine Word Problems
Finite String Recognizer
Exit conditions from S1: recognizes strings of form …0 (no 1 seen)
loop back to S1 if input is 0
Exit conditions from S4: recognizes strings of form …1 (no 0 seen)
loop back to S4 if input is 1
S0
[0]
S1
[0]
S2
[0]
S3
[1]
S4
[0]
S5
[0]
S6
[0]
Reset
0
1
0
1
0
0
0,1
1
0
…010
…100
…0
…1
0
1
…01
…10

## Slide 44: Finite State Machine Word Problems
Finite String Recognizer
S2, S5 with incomplete transitions
S2 = …01; If next input is 1, then string could be prefix of (01)1(00)
S4 handles just this case!
S5 = …10; If next input is 1, then string could be prefix of (10)1(0)
S2 handles just this case!
Final State Diagram
…010
S0
[0]
S1
[0]
S2
[0]
S3
[1]
S4
[0]
S5
[0]
S6
[0]
Reset
0
1
0
1
0
0
0,1
1
0
…100
…0
…1
0
1
…01
…10
1
1

## Slide 45: Finite State Machine Word Problems
Finite String Recognizer
module string
title '010/100 string recognizer state machine
Josephine Engineer, Itty Bity Machines, Inc.'
u1 device 'p22v10';
"Input Pins
clk, X, RESET pin 1, 2, 3;
"Output Pins
Q0, Q1, Q2, Z pin 19, 20, 21, 22;
Q0, Q1, Q2, Z istype 'pos,reg';
"State registers
SREG = [Q0, Q1, Q2, Z];
S0 = [0,0,0,0]; " Reset state
S1 = [0,0,1,0]; " strings of the form ...0
S2 = [0,1,0,0]; " strings of the form ...01
S3 = [0,1,1,1]; " strings of the form ...010
S4 = [1,0,0,0]; " strings of the form ...1
S5 = [1,0,1,0]; " strings of the form ...10
S6 = [1,1,0,0]; " strings of the form ...100
equations
[Q0.ar, Q1.ar, Q2.ar, Z.ar] = RESET; "Reset to S0
state_diagram SREG
state S0: if X then S4 else S1;
state S1: if X then S2 else S1;
state S2: if X then S4 else S3;
state S3: if X then S2 else S6;
state S4: if X then S4 else S5;
state S5: if X then S2 else S6;
state S6: goto S6;
test_vectors ([clk, RESET, X] -> [Z])
[0,1,.X.] -> [0];
[.C.,0,0] -> [0];
[.C.,0,0] -> [0];
[.C.,0,1] -> [0];
[.C.,0,0] -> [1];
[.C.,0,1] -> [0];
[.C.,0,0] -> [1];
[.C.,0,1] -> [0];
[.C.,0,0] -> [1];
[.C.,0,0] -> [0];
[.C.,0,1] -> [0];
[.C.,0,0] -> [0];
end string;
ABEL Description

## Slide 46: Finite State Machine Word Problems
Finite String Recognizer
Review of Process:
• Write down sample inputs and outputs to understand specification
• Write down sequences of states and transitions for the sequences
to be recognized
• Add missing transitions; reuse states as much as possible
• Verify I/O behavior of your state diagram to insure it functions
like the specification

## Slide 47: Finite State Machine Word Problems
Complex Counter
A sync. 3 bit counter has a mode control M. When M = 0, the counter
counts up in the binary sequence. When M = 1, the counter advances
through the Gray code sequence.
Binary: 000, 001, 010, 011, 100, 101, 110, 111
Gray: 000, 001, 011, 010, 110, 111, 101, 100
Valid I/O behavior:
Mode Input M
0
0
1
1
1
0
0
Current State
000
001
010
110
111
101
110
Next State (Z2 Z1 Z0)
001
010
110
111
101
110
111

## Slide 48: Finite State Machine Word Problems
Complex Counter
One state for each output combination
Add appropriate arcs for the mode control
Reset
S0
[000]
S1
[001]
S2
[010]
S3
[011]
S4
[100]
S5
[101]
S6
[110]
S7
[111]
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1

## Slide 49: Finite State Machine Word Problems
Complex Counter
module counter
title 'combination binary/gray code upcounter
Josephine Engineer, Itty Bity Machines, Inc.'
u1 device 'p22v10';
"Input Pins
clk, M, RESET pin 1, 2, 3;
"Output Pins
Z0, Z1, Z2 pin 19, 20, 21;
Z0, Z1, Z2 istype 'pos,reg';
"State registers
SREG = [Z0, Z1, Z2];
S0 = [0,0,0];
S1 = [0,0,1];
S2 = [0,1,0];
S3 = [0,1,1];
S4 = [1,0,0];
S5 = [1,0,1];
S6 = [1,1,0];
S7 = [1,1,1];
equations
[Z0.ar, Z1.ar, Z2.ar] = RESET; "Reset to state S0
state_diagram SREG
state S0: goto S1;
state S1: if M then S3 else S2;
state S2: if M then S6 else S3;
state S3: if M then S2 else S4;
state S4: if M then S0 else S5;
state S5: if M then S4 else S6;
state S6: goto S7;
state S7: if M then S5 else S0;
test_vectors ([clk, RESET, M] -> [Z0, Z1, Z2])
[0,1,.X.] -> [0,0,0];
[.C.,0,0] -> [0,0,1];
[.C.,0,0] -> [0,1,0];
[.C.,0,1] -> [1,1,0];
[.C.,0,1] -> [1,1,1];
[.C.,0,1] -> [1,0,1];
[.C.,0,0] -> [1,1,0];
[.C.,0,0] -> [1,1,1];
end counter;
ABEL Description

## Slide 50: Finite State Machine Word Problems
Traffic Light Controller
A busy highway is intersected by a little used farmroad. Detectors
C sense the presence of cars waiting on the farmroad. With no car
on farmroad, light remain green in highway direction. If vehicle on
farmroad, highway lights go from Green to Yellow to Red, allowing
the farmroad lights to become green. These stay green only as long
as a farmroad car is detected but never longer than a set interval.
When these are met, farm lights transition from Green to Yellow to
Red, allowing highway to return to green. Even if farmroad vehicles
are waiting, highway gets at least a set interval as green.
Assume you have an interval timer that generates a short time pulse
(TS) and a long time pulse (TL) in response to a set (ST) signal. TS
is to be used for timing yellow lights and TL for green lights.

## Slide 51: Finite State Machine Word Problems
Traffic Light Controller
Picture of Highway/Farmroad Intersection:

## Slide 52: Finite State Machine Word Problems
Traffic Light Controller
• Tabulation of Inputs and Outputs:
Input Signal
reset
C
TS
TL
Output Signal
HG, HY, HR
FG, FY, FR
ST
Description
place FSM in initial state
detect vehicle on farmroad
short time interval expired
long time interval expired
Description
assert green/yellow/red highway lights
assert green/yellow/red farmroad lights
start timing a short or long interval
• Tabulation of Unique States: Some light configuration imply others
State
S0
S1
S2
S3
Description
Highway green (farmroad red)
Highway yellow (farmroad red)
Farmroad green (highway red)
Farmroad yellow (highway red)

## Slide 53: Finite State Machine Word Problems
Traffic Light Controller
Refinement of ASM Chart:
Start with basic sequencing and outputs:

## Slide 54: Finite State Machine Word Problems
Traffic Light Controller
Determine Exit Conditions for S0:
Car waiting and Long Time Interval Expired- C • TL
Equivalent ASM Chart Fragments

## Slide 55: Finite State Machine Word Problems
Traffic Light Controller
S1 to S2 Transition:
Set ST on exit from S0
Stay in S1 until TS asserted
Similar situation for S3 to S4 transition

## Slide 56: Finite State Machine Word Problems
Traffic Light Controller
S2 Exit Condition: no car waiting OR long time interval expired
Complete ASM Chart for Traffic Light Controller

## Slide 57: Finite State Machine Word Problems
Traffic Light Controller
Compare with state diagram:
Advantages of State Charts:
• Concentrates on paths and conditions for exiting a state
• Exit conditions built up incrementally, later combined into
single Boolean condition for exit
• Easier to understand the design as an algorithm
S0: HG
S1: HY
S2: FG
S3: FY

## Slide 58: Finite State Machine Word Problems
Traffic Light Controller
module traffic
title 'traffic light FSM'
u1 device 'p22v10';
"Input Pins
clk, C, RESET, TS, TL
pin 1, 2, 3, 4, 5;
"Output Pins
Q0, Q1, HG, HY, HR,
FG, FY, FR, ST
pin 14, 15, 16, 17, 18,
19, 20, 21, 22;
Q0, Q1 istype 'pos,reg';
ST, HG, HY, HR,
FG, FY, FR istype 'pos,com';
"State registers
SREG = [Q0, Q1];
S0 = [ 0, 0];
S1 = [ 0, 1];
S2 = [ 1, 0];
S3 = [ 1, 1];
equations
[Q0.ar, Q1.ar] = RESET;
HG = !Q0 & !Q1;
HY = !Q0 & Q1;
HR = (Q0 & !Q1) # (Q0 & Q1);
FG = Q0 & !Q1;
FY = Q0 & Q1;
FR = (!Q0 & !Q1) # (!Q0 & Q1);
state_diagram SREG
state S0: if (TL & C) then S1 with ST = 1
else S0 with ST = 0
state S1: if TS then S2 with ST = 1
else S1 with ST = 0
state S2: if (TL # !C) then S3 with ST = 1
else S2 with ST = 0
state S3: if TS then S0 with ST = 1
else S3 with ST = 0
test_vectors
([clk,RESET, C, TS, TL]->[SREG,HG,HY,HR,FG,FY,FR,ST])
[.X., 1,.X.,.X.,.X.]->[ S0, 1, 0, 0, 0, 0, 1, 0];
[.C., 0, 0, 0, 0]->[ S0, 1, 0, 0, 0, 0, 1, 0];
[.C., 0, 1, 0, 1]->[ S1, 0, 1, 0, 0, 0, 1, 0];
[.C., 0, 1, 0, 0]->[ S1, 0, 1, 0, 0, 0, 1, 0];
[.C., 0, 1, 1, 0]->[ S2, 0, 0, 1, 1, 0, 0, 0];
[.C., 0, 1, 0, 0]->[ S2, 0, 0, 1, 1, 0, 0, 0];
[.C., 0, 1, 0, 1]->[ S3, 0, 0, 1, 0, 1, 0, 0];
[.C., 0, 1, 1, 0]->[ S0, 1, 0, 0, 0, 0, 1, 0];
end traffic;
ABEL Description

## Slide 59: Finite State Machine Word Problems
Digital Combination Lock
"3 bit serial lock controls entry to locked room. Inputs are RESET,
ENTER, 2 position switch for bit of key data. Locks generates an
UNLOCK signal when key matches internal combination. ERROR
light illuminated if key does not match combination. Sequence is:
(1) Press RESET, (2) enter key bit, (3) Press ENTER, (4) repeat (2) &
(3) two more times."
Problem specification is incomplete:
• how do you set the internal combination?
• exactly when is the ERROR light asserted?
Make reasonable assumptions:
• hardwired into next state logic vs. stored in internal register
• assert as soon as error is detected vs. wait until full combination
has been entered
Our design: registered combination plus error after full combination

## Slide 60: Finite State Machine Word Problems
Digital Combination Lock
Understanding the problem: draw a block diagram …
Internal
Combination
Operator Data
Inputs:
Reset
Enter
Key-In
L0, L1, L2
Outputs:
Unlock
Error

## Slide 61: Finite State Machine Word Problems
Digital Combination Lock
Enumeration of states:
what sequences lead to opening the door?
error conditions on a second pass …
START state plus three key COMParison states
START entered on RESET
Exit START when ENTER is pressed
Continue on if Key-In matches L0

## Slide 62: Finite State Machine Word Problems
Digital Combination Lock
Path to unlock:
Wait for
Enter Key press
Compare Key-IN

## Slide 63: Finite State Machine Word Problems
Digital Combination Lock
Now consider error paths
Should follow a similar sequence as UNLOCK path, except
asserting ERROR at the end:
COMP0 error exits to IDLE0'
COMP1 error exits to IDLE1'
COMP2 error exits to ERROR3

## Slide 64: Finite State Machine Word Problems
Digital Combination Lock
Equivalent State Diagram

## Slide 65: Finite State Machine Word Problems
Combination Lock
module lock
title 'comb. lock FSM'
u1 device 'p22v10';
"Input Pins
clk, RESET, ENTER, L0, L1, L2, KI
pin 1, 2, 3, 4, 5, 6, 7;
"Output Pins
Q0, Q1, Q2, Q3, UNLOCK, ERROR
pin 16, 17, 18, 19, 14, 15;
Q0, Q1, Q2, Q3 istype 'pos,reg';
UNLOCK, ERROR istype 'pos,com';
"State registers
SREG = [Q0, Q1, Q2, Q3];
START = [ 0, 0, 0, 0];
COMP0 = [ 0, 0, 0, 1];
IDLE0 = [ 0, 0, 1, 0];
COMP1 = [ 0, 0, 1, 1];
IDLE1 = [ 0, 1, 0, 0];
COMP2 = [ 0, 1, 0, 1];
DONE = [ 0, 1, 1, 0];
IDLE0p = [ 0, 1, 1, 1];
ERROR1 = [ 1, 0, 0, 0];
IDLE1p = [ 1, 0, 0, 1];
ERROR2 = [ 1, 0, 1, 0];
ERROR3 = [ 1, 0, 1, 1];
equations
[Q0.ar, Q1.ar, Q2.ar, Q3.ar] = RESET;
UNLOCK = !Q0 & Q1 & Q2 & !Q3;"asserted in DONE
ERROR = Q0 & !Q1 & Q2 & Q3; "asserted in ERROR3
state_diagram SREG
state START: if (RESET # !ENTER)
then START else COMP0;
state COMP0: if (KI == L0) then IDLE0 else IDLE0p;
state IDLE0: if (!ENTER) then IDLE0 else COMP1;
state COMP1: if (KI == L1) then IDLE1 else IDLE1p;
state IDLE1: if (!ENTER) then IDLE1 else COMP2;
state COMP2: if (KI == L2) then DONE else ERROR3;
state DONE: if (!RESET) then DONE else START;
state IDLE0p:if (!ENTER) then IDLE0p else ERROR1;
state ERROR1:goto IDLE1p;
state IDLE1p:if (!ENTER) then IDLE1p else ERROR2;
state ERROR2:goto ERROR3;
state ERROR3:if (!RESET) then ERROR3 else START;
test_vectors
end lock;

## Slide 66: Chapter Review
Basic Timing Behavior an FSM
• when are inputs sampled, next state/outputs transition and stabilize
• Moore and Mealy (Async and Sync) machine organizations
outputs = F(state) vs. outputs = F(state, inputs)
First Two Steps of the Six Step Procedure for FSM Design
• understanding the problem
• abstract representation of the FSM
Abstract Representations of an FSM
• ASM Charts, Hardware Description Languages
Word Problems
• understand I/O behavior; draw diagrams
• enumerate states for the "goal"; expand with error conditions
• reuse states whenever possible